## Slide 1: Working Under Pressure
Understanding the “push” in Fluid Power
An Introduction to Fluid Power

## Slide 2
Upper Atmosphere
Temperature is 68° F
Relative Humidity is 36%
How much does the column of air weigh???
14.7 Pounds
Square Inches
That means that there is a force of 14.7 pounds on each square inch of surface area,
or 14.7 psi.
Sea Level
Column of Air
Photo by Karen Helgerson

## Slide 3
Blaise Pascal,
the French physicist, found that a confined fluid transmits externally applied pressure uniformly in all directions and that the resultant force is applied perpendicular to the walls of the container and is described as the pressure per unit area of the container walls.
Blaise Pascal
It is from his research that we have the simple formula of
F=PA
Where:
A = Area acted upon
F = Force
P = Pressure x unit area
10

## Slide 4
Given a surface area of 12”,
if we apply a load of 14.7 pounds,
we have 14.7 pounds/square inch, or 14.7 psi.
However, if we have 162”,
and apply 14.7 pounds to each square inch,
we will still have 14.7 psi
but, using our formula of F = PA,
we find that our Force = 14.7 psi x 162”, or 235.2 pounds of force.
= 14.7 Pounds
= 12”
235.2 Pounds

## Slide 5
What if we are given a surface area of 1/42” and we apply a load of 14.7 pounds?
What will be the psi?
= 14.7 Pounds
= 1/42”
235.2
How many ¼ square inches are there in 1 square inch?
We now have the equivalent of 14.7 pounds acting on 16 locations for a total of
But the 235.2 pounds is acting on 1 square inch so the psi is
psi
Pounds

## Slide 6
If I hold up a piece of paper that is 8 1/2” x 11”, it will have 14.7 pounds acting on each square inch or…
1,374 pounds of force.
So, how is that I can easily hold up the piece of paper?
Remember, the force is acting on the entire surface area.
That means that there are 1,374 pounds pressing down on the top
but also 1,374 pounds pushing up from the bottom.
1,374 pounds
1,374 pounds
And to be totally correct, there is a force along each edge of the paper which can be calculated by the thickness of the paper times the length of the side times the pressure.
.50 pounds
.50 pounds
.65 pounds
.65 pounds

## Slide 7
0
10
20
30
Atmosphere
←
Atmosphere + Load Pressure
→
psig
psia
Our pressure gauges typically indicate the pressure difference between what we are measuring and the atmospheric pressure.
In our hydraulic systems where we operate in thousands of psi, the difference between psig and psia is often insignificant and usually does not need to be considered.
However, in our pneumatic systems, atmospheric pressure is a much higher percentage of the psig and often needs to be considered.
If our gauge reads 0 psi, it means that there is no difference between the load pressure and the atmospheric pressure.
The actual pressure is 1 atmosphere or 14.7 psi.
To distinguish between the two, we use the terms
psig
and
psia.
psig stands for gauge pressure and psia stands for absolute pressure.
0
10
20
30
40
50
60
-14.7
-10

## Slide 8
0
10
20
30
Atmosphere
←
Atmosphere minus Load Pressure
←
psig
psia
0
10
20
30
40
50
60
-14.7
-10
If we have a load pressure that is lower than atmospheric pressure,
then we will get a negative reading on our psig scale
and our psia indicator will move toward 0.

## Slide 9
14.7 psia
14.7 psia
13.0 psia
You are thirsty and you decide you get a drink.
You use a straw.
You are down by the beach, the temperature is 68° F, the relative humidity is 36% and so you know that the atmospheric pressure is…
That pressure is pushing down on the surface of the liquid both outside and inside the straw.
Why is it that when you begin to suck on the straw, the liquid flows up into your mouth???
You created a differential pressure that resulted in a differential force which caused the liquid to be pushed up into the straw.
Fluid always travels from higher pressure to lower pressure.*
Whenever there is flow, there is a pressure differential.

## Slide 10
We start with a square piston
with 92”of area,
We enclose the piston with a square tube.
The ends of the tube are open to atmosphere
and so 14.7 psia is applied to both sides of the piston
producing a force of 132.3 pounds at each side.
132.3 pounds
132.3 pounds
14.7 psia
14.7 psia
How can we make the piston move within the square tube?

## Slide 11
132.3 pounds
132.3 pounds
14.7 psia
14.7 psia
We have to change the force relationship between the two sides.
We can do this by increasing the force (pressure) on one side
or by decreasing the force (pressure) on one side.
14.0 psia
126.0 pounds
By decreasing the pressure on the right to 14 psia,
the force is decreased to 126 pounds
forcing the piston to move.

## Slide 12
132.3 pounds
132.3 pounds
14.7 psia
14.7 psia
How can we make the piston move within the square tube?
We have to change the force relationship between the two sides.
We can do this by increasing the force (pressure) on one side
or by decreasing the force (pressure) on one side.
15.0 psia
135.0 pounds
By increasing the pressure on the left to 15 psia,
the force is increased to 135 pounds
forcing the piston to move.

## Slide 13
We take the same square piston
with 92”of area,
We enclose the piston with a square tube,
and supply 1000 psi of
pressure to the piston.
We will develop a force of 1000 psig x 92”.
F = 9,000 Pounds
9,000
and add a 1” rod.
1000 psig
Sizing Cylinders…

## Slide 14
1000 psig
Now we will turn our cylinder around and see what happens when we apply the same pressure to the Rod end.
With 92” of area on the piston and with a 12” rod, we see that the rod takes up some space in the rod end and reduces the effective area of the piston.
The 12” of the rod is deducted from the area of the piston and we now have an effective area of 82”
We will now have a pulling force of 1000 psig x 82”, or 8,000 Pounds.
8,000
The retracting force of a single rod cylinder will always be less than the extending force if the pressure remains the same.

## Slide 15
When choosing a cylinder it is always best to start with the load that the cylinder will have to control.
The load will provide the necessary information about the force that the cylinder will need to develop.
Next we need to find out how much pressure is available.
Once the force and the available pressure are known, we can reach back to Blaise Pascal for help.
F=PA
F
P
A
You may like to use this triangle to remind you that F=PA, A=F/P, and P=F/A
F=
P
A
F
P=
A
F
The triangle works as you pull a letter out and place an equal sign after it. What remains in the pyramid will equal the item that was removed.
A=
P

## Slide 16
When applying Fluid Power, we create a pressure differential that causes the fluid to push toward lower pressure.
The fluid will push against whatever is in its way in order to get to the lowest pressure.
We use this pushing effort to perform useful work.
We usually contain the fluid in some type of tubing or pipe so that we can control its direction.
If we do not contain it, it is like the wind or a stream where gravity and/or velocity determine the available force.
Water wheel
Windmill
Combustion engine
Air plane
Brakes
It is what moves the

## Slide 17
In a dynamic system such as a water wheel or a turbine,
we direct the fluid flow to the device we want to move.
There is a pressure induced by gravity and the velocity of the fluid.
The paddles of the wheel are in the way of the fluid trying to get to the lower pressure area so the fluid pushes on the paddles and causes the wheel to spin.
If there was enough resistance to the movement of the wheel, the fluid would continue to run and simply go around the barrier.

## Slide 18
In a dynamic system such as a water wheel or a turbine,
we direct the fluid flow to the device we want to move.
There is a pressure induced by gravity and the velocity of the fluid.
The paddles of the wheel are in the way of the fluid trying to get to the lower pressure area so the fluid pushes on the paddles and causes the wheel to spin.
If there was enough resistance to the movement of the wheel, the fluid would continue to run and simply go around the barrier.

## Slide 19
100
Here we have a container filled with liquid having an inside area of 1 square inch connected to another container with an inside area of 10 square inches.
1² inch
10² inches
2.5”
.25”
10
?
10 psig
If we assign a weight of 10 pounds to our small piston,
We will add a piston to each side.
what will be the pressure in the system?
How heavy will the large piston have to be in order to balance the system?
So we see that with a force of only 10 pounds we are able to support an opposing force of 100 pounds.
However,
there is no free lunch!
When we try to actually move the load
we find that moving the small piston 2.5 inches causes the large piston to move
only .25”.
Just as in any mechanical system, force x distance is a constant.
10 x 2.5 = 100 x .25

## Slide 20
What would happen if our tubing were filled with air instead of liquid?
100
1² inch
10² inches
2.5”
.25”
10
?
10 psig
What would be the fluid pressure in psig?
What would be the fluid pressure in psia?
24.7 psia
The air would compress to about .6 the original volume.

## Slide 21
100
1² inch
10² inches
2.5”
.25”
10
10 psig
Once the air has been compressed, the pressure is the same as in the liquid system.
We again see that a 10 pound effort can support a 100 pound load.
We can also see that our advantage is offset by a loss in distance traveled.
The primary differences between pneumatics and hydraulics are the compressibility of the fluid and the pressures at which we operate.

## Slide 22
How a gear pump works
Two gears with parallel axes
are confined in a housing.
One is the drive gear, often keyed.
The other is the driven gear.
When sufficient rotational force is applied to the drive gear shaft, the gears begin to spin.
High pressure fluid pushes back against the gears, creating an unbalanced bearing load.
Low pressure fluid is drawn into the expanding opening as the gears separate.
It is then swept around the gear cavity until it is squeezed out as the teeth mesh again.
To balance the load, many pumps have a channel that exposes pressurized fluid about half way around the gears.
This pressurized fluid pushes back and helps balance the bearing load.